## Slide 1
Information”
Information”
Air Conditioner With PI Controller
Baran KALECIKLI 21290219
2025
Funding Information
This project received no external funding.
Acknowledgments
Prof. Dr. Asım Egemen YILMAZ
Kaan Can YILMAZ
“Funding Information”
Sponsors
This project does not have any sponsorship.
Abstract
Methodology
Conclusion
Background
Future Work
Results and Dıscussıon
In this project, I develop a smart temperature regulation system in Python which utilizes a classical PI (Proportional-Integral) controller combined with a lightweight time-series forecasting method based on linear regression. The goal is to stabilize the indoor temperature at a predefined comfort level (20°C), regardless of outdoor weather fluctuations. Using actual hourly outdoor temperature data collected for Ankara in 2025, the system simulates the thermal behavior of an indoor environment under realistic conditions. The controller dynamically adjusts the heating/cooling effect based on the error between the target and predicted indoor temperature, integrating both short-term trends and accumulated error over time. Unlike static threshold-based control, the use of regression allows the system to anticipate future deviations and respond proactively, leading to smoother and more stable control. In addition to the main model, alternative versions have also been developed where a PID controller is used without any regression-based forecasting. These variations serve as a baseline to assess the benefits of prediction-assisted control versus reactive-only strategies. Simulation results demonstrate that the indoor temperature converges to the target value with minimal oscillation, and the system remains robust under various external conditions. This approach shows potential for real-time embedded applications such as smart thermostats or IoT-based climate control systems, offering both energy efficiency and user comfort.
Climate control in buildings is a fundamental aspect of ensuring thermal comfort and energy efficiency. Traditional thermostatic systems often rely on static thresholds and do not adapt to environmental changes in real-time. PI (Proportional-Integral) controllers are widely used in industrial applications due to their simplicity and effectiveness in maintaining system stability. However, most conventional systems react only to current temperature readings, which may lead to delayed or oscillatory responses under varying environmental conditions. With the increasing availability of environmental data and computational power, integrating forecasting techniques such as linear regression into control loops opens the door for smarter and more anticipatory climate systems. Predictive elements allow the system to take proactive action rather than simply responding to observed errors. In this project, synthetic but realistic outdoor temperature data for Ankara in 2025 was manually generated to simulate hourly variations across seasonal cycles. This enabled consistent and controlled testing of the proposed models. Multiple models were designed and evaluated: one using a PI controller with regression-based temperature forecasting, and others using only reactive PID control strategies without forecasting. This allowed performance comparisons between proactive and reactive control approaches in terms of convergence, stability, and response speed.
In this project, a PI controller assisted by a linear regression model was successfully implemented to regulate indoor temperature based on outdoor conditions. The integration of a predictive model enhanced the controller's ability to maintain a comfortable indoor environment by anticipating future temperature trends. The system responded adaptively to seasonal changes and prevented overreaction by considering outdoor influences in the control logic. As a result, indoor temperature was consistently maintained within the targeted comfort range of 19°C to 21°C throughout the year. This approach demonstrates the potential of combining classical control with data-driven prediction to improve energy efficiency and thermal comfort in climate control systems.
Incorporate nonlinear regression models (e.g., decision trees or neural networks) to improve prediction accuracy under complex environmental conditions.
Extend the system to multi-zone buildings, enabling room-specific control and optimization.
Integrate real-time sensor feedback and IoT connectivity for cloud-based data logging and remote adjustment.
After the initial 4-day adaptation phase, the PI controller was activated and ran continuously throughout the year. The controller was tuned to maintain the indoor temperature around 20°C, within the desired comfort range. As shown in Figure 1, the outdoor temperature exhibited significant seasonal fluctuations. However, the indoor temperature remained relatively stable and well-regulated due to the controller’s intervention. The control output dynamically responded to the temperature difference, increasing during cold or hot periods and stabilizing when conditions approached the target. The plotted results clearly show that the system succeeded in keeping the indoor temperature within acceptable bounds, effectively filtering outdoor variations. Compared to similar studies in the literature that use PID-based or model-predictive HVAC systems, our approach using a simplified PI controller combined with short-term linear regression achieved comparable indoor stability with reduced computational complexity. Overall, the results validate the system’s effectiveness and demonstrate that even with simple modeling assumptions, indoor comfort can be maintained reliably.
Figure 1
Dataset Generation:
A temperature dataset was generated in CSV format with a sampling interval of 15 minutes, reflecting the continental climate conditions observed in Ankara. The values were synthetically modeled to simulate realistic outdoor temperature variations over the course of one year.
2. Indoor Temperature Modeling:
The effect of outdoor temperature on indoor conditions was simulated using realistic thermal response behavior, without any active control for the initial period. This allowed the indoor environment to naturally respond to external changes, creating a baseline dataset.
3. Controller Initialization Constraints:
To prevent the PI controller from operating under unrealistic or unsafe thermal commands, the proportional and integral gains were carefully selected. Additionally, the control signal was limited to a safe operational range to avoid extreme HVAC behaviors.
4.Regression-Based Temperature Prediction:
In Python, the LinearRegression model from the sklearn.linear_model library was integrated into the project. The model was trained to predict the indoor temperature 15 minutes ahead using the last four recorded values as input features.
5. Adaptive PI Control Logic:
The PI controller was triggered based on the difference between the predicted future temperature and the desired target range. The magnitude of this difference influenced how aggressively the controller adjusted the system.
6. Initial Uncontrolled Phase:
During the first four days, the controller was deliberately kept inactive to allow the indoor temperature to evolve freely under outdoor influence. This phase also provided training data for the regression model.
7. Controlled Operation Period:
Following the initial phase, the PI controller operated continuously for the remainder of the year. It was tuned to maintain indoor temperature around 20°C within the desired comfort range.